## Slide 1: Electron Drift Instability in a Hall Thruster: Inside Particle-In-Cell Simulations
Laurent Garrigues, Directeur de Recherche CNRS
Laboratoire Plasma et Conversion d’Energie – LAPLACE
Université de Toulouse, CNRS-UPS-INPT
31062 Toulouse Cedex 09, France
laurent.garrigues@laplace.univ-tlse.fr

## Slide 2: Outline
Partially magnetized low temperature plasmas
Magnetized discharge: Hall Thruster
Electron drift instability via PIC simulations
Benchmark
Conclusions and perspectives

## Slide 3: Partially magnetized LTP
Partially magnetized discharges
  Electrons are magnetized
  Ions remain unmagnetized
DC discharge sustainment possible
  Low pressure ~ 0.1 – 10 mTorr (0.013-13 Pa)
  Gas density ~ 1018 - 1020 m-3
  Increasing residence time of electrons
  Hall parameter
  High ionization degree 10-3 – 0.1, strong neutral depletion
  Collisionless ions
Orders of magnitude
  Plasma densities ~ 1018 m-3
  Electron temperature 10 – 100 eV

## Slide 4: Partially magnetized LTP - ExB configurations
ExB configurations to enhance confinement
  Closed drift of electrons – cylindrical symmetry
  Ion sources applications (plasma processing, propulsion, NBI, etc.)
Interesting physical mechanisms to study
  Anomalous cross-field transport
  Rotating structures (cm and kHz ranges)
Gallian et al. PSST
22, 055012 (2013)
  Micro-instabilities (mm and MHz ranges)
Boeuf, Frontiers 2, 74 (2014)
B
E
anode
cathode
cathode
anode
Penning cell
B
E
anode
cathode
cathode
anode
Cylindrical
magnetron
S
N
S
B
E
planar
magnetron
anode
B
E
anode
collector
anode
Cybele (CEA), EPFL
Helicon
B
E
anode
collector
anode
Mistral
(PIIM)
Hot
e-
S
N
S
N
S
N
S
N
S

## Slide 5: Hall thruster geometry
cathode
anode
Xe injection
magnetic
circuit
coils
Xe+
Ion jet
channel
dielectric walls
Hall current
B
E
.

## Slide 6: Hall thrusters in the world
PPS®1350 Snecma on ESA Smart-1 probe
PPS20K Snecma
NASA/UM
6 kW HT
Russian – SPT100
http://pepl.engin.umich.edu
China – 200 W

## Slide 7: Hall thruster: characteristics
Principle
  Mfp << L
  Magnetic field strength: trap only electrons
  Ions are collisionless
Typical numbers
  Voltage: 300 V, current ~ 4 A
  Diameter: 10 cm, L = 2.5 cm
  Xe mass flow: 5 mg/s (density ~ 1020 m-3)
  Plasma density: 1018 m-3
  Electron temperature: 50 eV
Missions
  Very high ion velocity
  Well adapted for satellite station keeping
cathode
anode
Xe injection
magnetic
circuit
coils
Xe+
Ion jet
channel
dielectric walls

## Slide 8: Hall thruster operation
Anode
Cathode
Br
Exhaust
plane
Xe+
e-
Si
Xe
Gas injected (Xe easy to ionize, high mass)
e-
Ex
Local drop of conductivity high Ex inside the plasma
Va
DC discharge voltage between anode and cathode planes
0
e-
Electrons from cathode to neutralize ions

## Slide 9: Anomalous transport
Anode
Cathode
Br
e-
Ex
Plan
de sortie
e-
Xe+
e-
Si
Xe
Va
Almost full ionization of neutral gas (> 90 %)
Mechanism responsible for electron transport without collisions?
Instabilities can explain electron transport?
0

## Slide 10: Dispersion relation
System studied
  Electrons are magnetized, Maxwellian and collisionless
  Cold Ions, not magnetized and collisionless
  Coupling with Poisson’s equation
  Constant plasma and magnetic field
  Dispersion relation to study existence and growth rate of instabilities
Gary and Sanderson, J. Plasma Physics 4, 739 (1970)
Fornslund et al., Phys. Rev. Letter, 25, 1266 (1970)
Lampe et al., Phys. Rev. Letter, 22, 1221 (1971)
Ducrocq et al., Phys. Plasmas 13, 102111 (2013)
Cavalier et al., Phys. Plasmas 20, 082107 (2013)
Dispersion relation, electrostatic waves
Bz
Ex
x
y
z
: Gordeev function

## Slide 11: Transition to MIA instability?
MIA Characteristics
  Maximum growth rate
  Wave vector at maximum growth rate
  Angular frequency at maximum growth rate
  Amplitude of field oscillations
  Assuming saturation due to ion-wave trapping
T. Lafleur et al., PoP 23, 053503 (2016)
Wavelength
E = 200 V/cm, B = 200 G, ne ~ 1017 m-3, Te ~ 50 eV
Transition to modified acoustic instability
  If and
  Transition to MIA

## Slide 12: Hall thruster: ExB configuration
5 cm
R2
R1
3 cm
Azimuthal
drift
Ex×Br
Br
Ex
Bz
Ex
x
y
z
-Ex×Bz
Hall thruster characteristics
  Electrons are magnetized
  Ions are not magnetized
  Closed electron drift in the azimuthal direction
  Instabilities due to different velocity between electrons and ions in the azimuthal direction
=

## Slide 13: 2D PIC simplified model – (x,y) plane (1/2)
Bz
Ex
x
y
z
-Ex×Bz
0V
200V
J. P. Boeuf and L. Garrigues
PoP 25, 061204 (2018)
Explicit PIC method with OpenMP/MPI parallelization techniques
Rectangular simulation domain (x,y) directions
B to simulation plane (with fixed profile)
Periodic boundary conditions along y (angular sector, w = 1 cm)
d= 2.5 cm, cathode @ 2.4 cm
Applied voltage 200 V

## Slide 14: 2D PIC simplified model – (x,y) plane (2/2)
Bz
Ex
x
y
z
-Ex×Bz
Given source of injection of charged particles
  Changing JM means changing plasma density
No collisions
Vlasov-Poisson system

## Slide 15: 1D plasma properties – averaged y and t
(eV)
JM = 400 A/m2

## Slide 16: 2D plasma properties
min
max
0.0
0.5
1.0
1.5
2.0
2.5
0.0
0.25
0.5
1.0
0.75
-ExxBz
x (cm)
y (cm)
Ey
Bz
JM = 400 A/m2
- 5x104 V/m
+5x104 V/m
+5x1017 m-3
0

## Slide 17: Parametric study
J. P. Boeuf and L. Garrigues PoP 25, 061204 (2018)
- 1.1/1.5/3.5/5.5 x104 V/m
+1.1/1.5/3.5/5.5 x104 V/m
+0.4/1/2/4 x1017 m-3
0
x = 1 cm

## Slide 18: Numerical noise effect
0V
200V
JM

## Slide 19: Calculation of anomalous transport
@ the maximum of B field
Bz
x
y
z

## Slide 20: Landmark website
https://www.landmark-plasma.com/services

## Slide 21: Time-averaged axial electric field profile
Charoy et al., submitted (2019)

## Slide 22: Convergence

## Slide 23: Conclusions and perspectives
ExB discharges and mechanisms driving the operation of that systems are complex and poorly understood
Particle-In-Cell simulations can be an interesting tool to better understand what happens
Benchmarks are necessary to verify that mechanisms obtained are related to physics and not numerical artefacts
High plasma density require efficient parallelization techniques to model systems in 3D
Measurements validating numerical results needed

## Slide 24: Acknowledgments
RTRA, Sciences et Technologies de l’Aéronautique de l’Espace, Toulouse, IMPULSE project
Super calculators CALMIP/Olympe and CINECA/Marconi

## Slide 25: Ion trapping
Boeuf and Garrigues
PoP 25, 061204 (2018)
X
y
1.75
2

## Slide 26: Numerical models
Charoy et al., submitted (2019)